## Slide 1
Mengyuan Li*1, Luca Wilke*2, Jan Wichelmann2, Thomas Eisenbarth2, Radu Teodorescu1, Yinqian Zhang3
li.7533@osu.edu, l.wilke@uni-luebeck.de
1The Ohio State University, 2University of Lübeck, 3Southern University of Science and Technology *Equal Contribution
A Systematic Look at Ciphertext Side Channels
on AMD SEV-SNP
Notes: Good afternoon. My name is Mengyuan Li, I am from the ohio state university, This is Luca wilke, the co-first author from university of lubeck. it is a great honor to be here to present our paper. A Systematic Look at Ciphertext Side Channels
on AMD SEV-SNP
Other authors include Jan Wi chel mann2, Thomas Ei sen barth2 , from university of Lubec k, Radu Teodorescu1, Yinqian Zhang3 from southern University of Science and Technology

## Slide 2: Ciphertext Side Channel
  Widely exists in memory-encryption-based Trust Execution Environment (TEE).
  Challenges the memory encryption method used in large-memory TEEs.
  Hard to fix in a short time.
Notes: In this paper, we showed a new ciphertext side channel that widely exists in memory-encryption based Trusted Execution environment.
The ciphertext side channel challenges the memory encryption method used in TEE.
And just like cache side channel attacks, it might be difficult to fix in a short time.

## Slide 3: Cloud Computing
Limited Trust For Traditional Cloud Computing
  Cloud users cannot trust the Cloud Service Provider.
  Their sensitive data is under the threat of the potentially malicious Cloud Service Provider as well as other malicious tenants.
  Restricts many potential cloud computing scenarios.
Cloud Service Provider
Cloud Users
(Companies)
Other Cloud Users
Notes: I will start with some background information. trust might be one biggest problem in cloud computing.
  Cloud users cannot trust the Cloud Service Provider.
  Their sensitive data is in danger
  This, actually Restricts many potential cloud computing scenarios.

## Slide 4: Confidential Computing on Cloud
Confidential computing enables new public cloud scenarios
Confidential computing is enabled by some hardware-based security features: TEE
  Most TEEs protect cloud user’s data against both privileged software attackers and physical attackers
Notes: To solve this problem, industry and academia move their attention to confidential computing.
Confidential computing is achieved by some hardware-based features, which is called Trusted Execution environment (TEE).
  Most TEEs protect cloud user’s data against privilege software attackers (even the hypervisor) and physical attackers

## Slide 5
SGX
Application
OS
Enclave
Enclave
Intel CPU
SEV
VMM
VM
AMD CPU
VM
VM-based TEE
Code & binary Compatible
Enclave-based TEE
Confidential Computing with TEE
AMD SEV
Intel TDX
ARM CCA
…
Intel SGX
Keystone
Penglai
…
Notes: There are many exitsing TEE products, like enclave-based TEE,,
And also VM-based TEE, like AMD Secure encrypted virtualization (SEV), Intel TDX, ARM CCA,
For VM-based TEEs, they are aiming to protect the entire virtual machine, so they are very user-friendly, you don’t need to rewrite your code

## Slide 6
SGX
Application
OS
Enclave
Enclave
Intel CPU
SEV
VMM
VM
AMD CPU
VM
VM-based TEE
Code & binary Compatible
Enclave-based TEE
Confidential Computing with TEE
AMD SEV
Intel TDX
ARM CCA
…
Intel SGX
Keystone
PENGLAI
…
Notes: Because of this, AMD SEV is already be adopted by some CSP, including Google Cloud, Microsoft Azure and IBM cloud,
AMD SEV is also our focus for the paper, since it is the only commercial available VM-based TEE right now.

## Slide 7: Isolated Execution Environment on Chip
Compute
Hardware Protected
Trust Boundary
Data
Isolate a hardware-protected environment for secure data processing within the CPU chip
CPU
Notes: So how exactly TEE protect the data?
The key idea is to provide an isolated execution environment when data is within the CPU chip
figure is confusing
package,

## Slide 8: Memory Encryption: Protect against off-chip attackers
Compute
Data
Hardware Protected
Trust Boundary
Data
Using memory encryption for protecting data outside the CPU chip
Memory Encryption
Encrypted
CPU
RAM
RAM
Notes: When data goes out the CPU chip, the memory encryption seems to be the only way to protect data.
TEEs may use a memory encryption engine to automatically encrypt data and decrypt data when write to or read from the memory

## Slide 9: How Memory is Encrypted in SEV
VM’s memory is accessed randomly.
Notes: Then
Lets look at how AMD SEV implements the memory encryption. There are actually some restrictions, Because VM’s memory is accessed randomly.

## Slide 10: Memory Encryption in SEV
Cipher 1
Cipher 2
Cipher 3
Cipher 256
128-bit Block
Cipher 4
……
4KB page
0x000
0xff0
0x010
0x020
0x030
0000
0000
0000
0000
Plaintext
0000
……
4KB page
0x000
0xff0
0x010
0x020
0x030
VM’s memory is accessed randomly.
Notes: So the Memory is independently encrypted per aligned 128-bit block using AES encryption

## Slide 11: Memory Encryption in SEV
VM’s memory is accessed randomly.
To avoid inferring plaintext (m) via the same ciphertext (C).
Notes: And To avoid malicious hypervisor inferring plaintext (m) via the same ciphertext (C).

## Slide 12: Memory Encryption in SEV
VM’s memory is accessed randomly.
To avoid inferring plaintext (m) via the same ciphertext (C).
(m⊕)
128-bit Plaintext
T(sPA)
128-bit Ciphertext
Encryption
Notes: an additional physical address based tweak function T(x) is used here.

## Slide 13: Memory Encryption in SEV
VM’s memory is accessed randomly.
To avoid inferring plaintext (m) via the same ciphertext (C).
(m⊕)
128-bit Plaintext
T(sPA)
128-bit Ciphertext
Encryption
The same plaintext at the same location will have the same ciphertext during the VM’s lifecycle
The same plaintext at different locations will have different ciphertext
Notes: The consequence is obvious,
The same plaintext at different locations will have different ciphertext
But
The same plaintext at the same location will have the same ciphertext during the VM’s lifecycle
Meanwhile, SEV also allows hypervisor to have software-level access to the ciphertext.

## Slide 14
“Are current cryptography implementations running inside a TEE still safe when an attacker has access to the ciphertext of the encrypted memory?"
TEE Trust Boundary
AES Engine
DRAM
Application Data
Research Question
Software access
Physical
access
Deterministic
Encryption
Notes: In the paper,
We raised the following research question
“Are current cryptography implementations running inside a TEE still safe when an attacker has access to the ciphertext of the encrypted memory?"
The answer is no. it is not secure. Especially for TEEs that use a deterministic encryption
In the paper We show the side channel information caused by ciphertext changes is sufficient enough to leak key secret protected by SEV

## Slide 15: Ciphertext Side Channel - Outline
Attack Primitives
  Dictionary Attacks
  Collision Attacks
Mitigation
  Hardware-level Mitigation
  Software-level Mitigation
Conclusion
Notes: Lets talk about that in detail s. This is the outline. We will first introduce two possible attack primitives,

## Slide 16: Ciphertext Side Channel - Outline
Attack Primitives
  Dictionary Attacks
  Collision Attacks
Mitigation
  Hardware-level Mitigation
  Software-level Mitigation
Conclusion
Notes: We will begin with dictionary attacks

## Slide 17: Attack Primitives – Dictionary Attacks
128-bit Ciphertext Block
-
Secret
-
-
Dictionary Attacks: For a fixed address, building the ciphertext-plaintext dictionary and inferring the secret by repeated ciphertext.
Data1
Cipher2
Cipher3
Cipher4
Cipher2
Data2
Data3
Data4
Data2
1-to-1 Dictionary
Cipher1
Notes: The dictionary attack targets at a 128-bit block with fixed physical address.
attackers build a ciphertext-plaintext dictionary and infer the secret by repeated ciphertext.

## Slide 18: Exploit context switches inside the VM
Process 1
Kernel
Context Switch
Pt_regs
gPA1
Process 1
Kernel
Pt_regs
gPA1
OS context switch stores registers into some kernel structures (pt_regs)
Notes: Lets show you A dictionary attack case study about using some kernel structure to break ECDSA,
When there is OS context switch, kernel will store the process’s registers in a structure called Pt_registers, which is a pretty fixed address, so we don’t need to worry about the tweak function used in memory encryption.

## Slide 19: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Process 1
Kernel
Context Switch
Pt_regs
gPA1
Process 1
Kernel
Pt_regs
gPA1
General Steps:
Intercept the VM at some execution points
Record the ciphertext at pt_regs region
Notes: The general attack steps are pretty simple, the attacker only needs to
Intercept the VM at some execution points
Record the ciphertext at the pt_regs

## Slide 20: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
Notes: We will go through this case study step by step,
ECDSA constant time implementation uses a function called ec_scalar_multiply _ladder to generate a signature, we call this function function 2, and his guest physical address is GPA2,
And inside this function, BN_is_bit_Set is repeated called to get one bit of secret nonce k for future calculation. We call BN_is_bit_set function1, and its gpa is GPA1, And the nonce k is the secret the attacker wants to steal

## Slide 21: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
STEP1:
Locate gPA of F1 and F2.
-- PMC counter-based controlled channel tool
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
Notes: to Intercept the VM at certain execution points
The attacker first needs to locate the two target functions I mentioned, ,
Here we introduce a PMC-based Page-level Controlled Channel tool

## Slide 22: PMC-based Page-level Controlled Channel
gVA
gPA
Page 1
Page 2
Page 3
Page 4
Page 6
Unset all
P bit
HV can actively collect more information (PMC-based)
Page 5
NPF of Page 5 (gPA0)
NPF of Page 7 (gPA1)
NPF of Page 1 (gPA2)
….
Record PMC , P0
Record PMC , P1
Record PMC , P2
Δ P
Δ P’
….
NPF + PMC data allow precise tracking of execution state
Notes: In the tool, The attacker unset all present bit to trigger nested page falut , and meanwhile also uses some PMC events to collect additional information, like the number of retired instructions
When combine those information together, the attacker can locate certain code page or data page very precisely, and on-the-fly
we find this tool prtty useful when intercept The VM,
You may also find this tool in our github lnk

## Slide 23: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Step2:
Iteratively unset the present bit of F1 & F2 to intercept the VM.
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
Notes: Ok. After identifying the target functions, the second step will be iteratively unset the present bit of F1 & F2 to intercept the VM.

## Slide 24: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
……
……
NPF of F1 gPA1
NPF of F2 gPA2
Unset
P bit
NPF of F1 gPA1
NPF of F2 gPA2
NPF of F2 gPA2
Notes: Because there is a loop, The attacker then observes repeated NPFs of Function one and Function 2, which effectively intercept VM’s execution

## Slide 25: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Step3:
Get ciphertext at certain execution points.
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
Notes: After intercepting VM using NPF, the attacker only needs to get ciphertext at certain execution points.

## Slide 26: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Try to call F1 BN_is_bit_set()
Finish BN_is_bit_set(), try to return to F2
ith bit of k in RAX
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
……
NPF of F1 gPA1
NPF of F2 gPA2
NPF of F2 gPA2
Notes: Here In this case study, The attacker stop the VM when he intercept NPF of Function2,
Because, at this execution point, BN_is_bit_Set just finished, one bit of the secret is in RAX register right now, and the program is trying to return,

## Slide 27: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Try to call F1 BN_is_bit_set()
Finish BN_is_bit_set(), try to return to F2
ith bit of k in RAX
Not handle NPF (gPA2)
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
……
NPF of F1 gPA1
NPF of F2 gPA2
NPF of F2 gPA2
NPF of F2 gPA2
NPF of F2 gPA2
NPF of F2 gPA2
Notes: The attacker just keeps not handling the NPF,,

## Slide 28: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Try to call F1 BN_is_bit_set()
Finish BN_is_bit_set(), try to return to F2
ith bit of k in RAX
Not handle NPF (gPA2)
Store registers to pt_regs, go to kernel space
Query APIC Timer
(kernel behaviors)
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
……
NPF of F1 gPA1
NPF of F2 gPA2
NPF of F2 gPA2
NPF of F2 gPA2
Notes: and eventually, some time-driven interrupts will occupy.

## Slide 29: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Store registers to pt_regs, go to kernel space
Query APIC Timer
(kernel behaviors)
Read pt_regs
128-bit Ciphertext Block in pt_regs
RAX
Unchanged R8
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
NPF of F2 gPA2
Notes: When the attacker observe those interrupts, which means the VM switches to kernel right now, and the one bit of the secret should be stored in Pt_register,
the attacker then simply record the ciphertext ,

## Slide 30: Dictionary Attacks Case Study#1 – Steal ECDSA Nonce via pt_regs
Store registers to pt_regs, go to kernel space
Query APIC Timer
(kernel behaviors)
Read pt_regs
128-bit Ciphertext Block in pt_regs
RAX
Unchanged R8
Cipher1
Bit = 0
Cipher2
Bit = 1
Dictionary
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
For loop inside
F2 ec_scalar_mul_ladder()
{
…
F1 BN_is_bit_set(k, ith)
…
}
Constant-time Montgomery ladder implementation
NPF of F2 gPA2
Notes: Since within the 128-bit block, only RAX will change and only has two possible value 0, 1
So the attacker can easilly Build the dictionary, and use the dictionary to break the entire secret

## Slide 31: Ciphertext Side Channel - Outline
Attack Primitives
  Dictionary Attacks
  Collision Attacks
Mitigation
  Hardware-level Mitigation
  Software-level Mitigation
Conclusion
Notes: Thank you Mengyuan, I will take over for the rest of the presentation
After learning all about our first attack primitive, let's continue with the second one.

## Slide 32: Attack Primitives – Collision Attacks
128-bit Blocks
Cipher1
Cipher2
Cipher3
Cipher4
Requirement:
Ciphertext change or repeat is secret-dependent
-- Additional side-channel information than control flow information and cache side-channel information
Secret
Cipher1
Cipher5
Cipher3
Cipher4
Secret-dependent write behaviors
Change
Repeat
Repeat
Repeat

## Slide 33: Attack Primitives – Collision Attacks
Combine control flow tracking and code knowledge
Exploit patterns of secret dependent memory writes
Cipher1
Cipher2
Cipher5
Changed
Cipher6
Changed
Buffer A
Buffer B
Cipher1
Cipher2
Cipher2
Same
Cipher1
Same
Buffer A
Buffer B
Notes: The collision attack works similar to attacks on secret dependent control flow.
We require knowledge of the attacked code as well as a way to track the victims execution state, to know where we are in the code.
However, instead of observing branches or accesses to different memory locations depending on the secret, we observe value writes to a fixed location

## Slide 34: Attack Primitives – Collision Attacks
Combine control flow tracking and code knowledge
Exploit patterns of secret dependent memory writes
Notes: The collision attack works similar to attacks on secret dependent control flow.
We require knowledge of the attacked code as well as a way to track the victims execution state, to know where we are in the code.
In contrast to attacks on secret dependent control flow, we attack constant time code by observing certain memory write operations to fixed locations.
In contrast to the collision attack, we do not learn the plaintext values for ciphertext blcoks but infer secret internal state variables by ciphertext changes.
So let's look at an concrete example

## Slide 35: Collision Attacks Case Study#1 – Conditional Swap
Notes: Here, we se the code for a constant time swap operation.
This construction is commonly used to write constant time code, by first computing all possible outcomes and then using cswap to select the correct one
The important property of this code is that we always write to a and b, regardless whether the values are swapped or not
Probably don’t use
One time square only
Second time square and multiply
Select which outcome we want to keep

## Slide 36: Collision Attacks Case Study#1 – Conditional Swap
Selection Mask
Notes: First, we compute the selection mask, which will either be zero, or hex ff, depending on the value c

## Slide 37: Collision Attacks Case Study#1 – Conditional Swap
Prepare Update
Notes: Next, we compute the update value x, by first building the xor of a and b.
The and statement on the next line, clears x if mask was set to zero

## Slide 38: Collision Attacks Case Study#1 – Conditional Swap
Update Values
Notes: Final, we update the values in a and b by xoring them with the update value x
If x was set to zero, nothing happens.
If x still contains the xor of a and b, the two occurences of a will cancel each other out and a is updated to b
As the write is uniform, we achieve the constant time property
So how can we attack this with our capabilities?

## Slide 39: Collision Attacks Case Study#1 – Conditional Swap
Cipher1
Cipher2
C = 1
Cipher5
Changed
Cipher6
Changed
Buf a
Buf b
Cipher1
Cipher2
Cipher2
Same
Cipher1
Same
Buf a
Buf b
C = 0
Notes: We simply need to observe the value of a and b before and after the execution of the cswap operation as shown on the right hand side
The fact whether they have changed or not gives us the secret state c
Demonstranted in and end to end attack against EdDSA in openssh where the attacker simply has to send a handshake package to steal the secret key.

## Slide 40: Collision Attacks Case Study#1 – Steal ECDSA Nonce via Heap
gPA1: F1 BN_is_bit_set()
gPA2: F2 ec_scalar_mul_ladder()
Code segment of ec_scalar_mul_ladder()
NPF of F1 gPA1
NPF of F2 gPA2
NPF of F2 gPA2
……
NPF of F1 gPA1
NPF of F2 gPA2
……
Read Heap Page (gPA4)
in each iteration
Locate
C1
C2
N-byte r
N-byte s
C3
C4
C3
C4
C5
C6
……
Kbit = 1
Kbit = 0
Kbit = 1
……
Notes: Luca: I think this has a lot of repetition with the previous slide -> hidden the slide for now

## Slide 41: Ciphertext Side Channel - Outline
Attack Primitives
  Dictionary Attacks
  Collision Attacks
Mitigation
  Hardware-level Mitigation
  Software-level Mitigation
Conclusion
Notes: This concludes the attack part of the talk.
Let's continue with countermeasures

## Slide 42: Hardware-level mitigation – Add freshness
0000
Plaintext
Cipher 1
(m⊕CTR⊕ )
Write 1
0000
Update CTR
Cipher 2
Ciphertext
Challenges
Storage Overhead
Performance Overhead
Write 2

## Slide 43: Hardware-level mitigation – Add freshness
0000
Plaintext
Cipher 1
(m⊕CTR⊕ )
Write 1
0000
Update CTR
Cipher 2
Ciphertext
Challenges
Storage Overhead
Performance Overhead
Write 2
Probabilistic Encryption
Notes: The most holistic solution to this problem, is to use probabilistic encryption, e.g. with a counter value that is updated before each write.
This way even if we write the same plaintext to the same location two times, we get different ciphertexts.
Probabilistic encryption is of course not new and there are many such schemes out there
In the context of main memory encryption they face two main challenges
Storage overhead for the counters
And reduced performance due to fetching and updating the counters

## Slide 44: A General Ciphertext Side Channel
=> SGX on Ice Lake, TDX and CCA all use deterministic memory encryption
SGX and TDX prevent software access to ciphertext at some performance cost
Physical channels like bus intercept remain open
Notes: TODO: port slide to power point

## Slide 45: A General Ciphertext Side Channel
Name | Max Size | Encryption Mode
Intel SGX | 256 MB | AES-CTR + Integrity + Freshness
AMD SEV | No limit | XEX
Intel SGX on Ice Lake SP | Up to 1 TB | XEX
Intel TDX | No limit | XTS + Integrity
ARM CCA | No limit | XTS or QARMA
Notes: In fact,
looking at the currently available TEE designs for large memory, we see that none of them use a probabilistic crypto system
Only the old SGX version with very limited memory size uses the holy grail of cryptography with freshness and integrity

## Slide 46: A General Ciphertext Side Channel
=> SGX on Ice Lake, TDX and CCA all use deterministic memory encryption
SGX and TDX prevent software access to ciphertext at some performance cost
Physical channels like bus intercept remain open
Name | Max Size | Encryption Mode | Vulnerable to software access | Vulnerable to physical access
Intel SGX | 256 MB | AES-CTR + Integrity + Freshness | No | No
AMD SEV | No limit | XEX | Yes | Yes
Intel SGX on Ice Lake SP | Up to 1 TB | XEX | No | Yes
Intel TDX | No limit | XTS + Integrity | No | Yes
ARM CCA | No limit | XTS or QARMA | ? | Yes
Notes: However, for the two Intel solutions, we do not have access to the ciphertexts via software.
Thus we cannot carry out the attack as a software only attacker, like for AMD SEV

## Slide 47: A General Ciphertext Side Channel
=> SGX on Ice Lake, TDX and CCA all use deterministic memory encryption
SGX and TDX prevent software access to ciphertext at some performance cost
Physical channels like bus intercept remain open
Name | Max Size | Encryption Mode | Vulnerable to software access | Vulnerable to physical access
Intel SGX | 256 MB | AES-CTR + Integrity + Freshness | No | No
AMD SEV | No limit | XEX | Yes | Yes
Intel SGX on Ice Lake SP | Up to 1 TB | XEX | No | Yes
Intel TDX | No limit | XTS + Integrity | No | Yes
ARM CCA | No limit | XTS or QARMA | ? | Yes
Notes: Nonetheless, a physical attack could still carry out the attacks by observing the physical memory, e.g. by interposing the memory bus
So in principal these systems remain vulnerable to a physical attacker

## Slide 48: Hardware-level mitigation – Add freshness
Cipher 1
Cipher 2
Cipher 3
Cipher 256
128-bit Block
Cipher 4
……
4KB page
0x000
0xff0
0x010
0x020
0x030
(m⊕CTR⊕ )
0000
0000
0000
0000
Plaintext
0000
……
4KB page
0x000
0xff0
0x010
0x020
0x030
Storage Overhead
Performance Overhead?
Freshness is not introduced in SEV, CCA， TDX
Notes: Luca: TODO:
- fix alignment
- Figure does not make to much sense. I think we should explain this with a sequence of memory snapshots where a value repeats. This really
Showcases the reasoning for freshness

## Slide 49: Hardware-level mitigation – Add freshness
Cipher 1
Cipher 2
Cipher 3
Cipher 256
128-bit Block
Cipher 4
……
4KB page
0x000
0xff0
0x010
0x020
0x030
(m⊕CTR⊕ )
0000
0000
0000
0000
Plaintext
0000
……
4KB page
0x000
0xff0
0x010
0x020
0x030
Storage Overhead
Performance Overhead?
Freshness is not introduced in SEV, CCA， TDX
Notes: Luca: TODO:
- fix alignment
- Figure does not make to much sense. I think we should explain this with a sequence of memory snapshots where a value repeats. This really
Showcases the reasoning for freshness

## Slide 50: Ciphertext Side Channel - Outline
Attack Primitives
  Dictionary Attacks
  Collision Attacks
Mitigation
  Hardware-level Mitigation
  Software-level Mitigation
Conclusion
Notes: Since we do not have TEEs for large memory with probabilistic encryption, we should also have a way to solve this problem in software.

## Slide 51: Software Level Mitigations: Basic Strategies
Change location for each write
Memory
Cipher 1
Cipher 2
Register Space
Plain
Plain
Notes: There are two basic Strategies
The first one is to change the memory location each time we write our secret
This way, a different tweak is used at the new memory location, mimicking probabilistic encryption

## Slide 52: Software Level Mitigations: Basic Strategies
Change location for each write Mask values before write
Memory
Cipher 1
Cipher 2
Cipher 3
Register Space
Plain
Plain
Plain + Mask A
Plain
Notes: The second strategy is too to add a counter/mask while processing the secret on the register level
Whenwe read from memory we have to unmask the value first
Before writing back we choose a new mask

## Slide 53: Software Level Mitigations: Basic Strategies
Change location for each write Mask values before write
Memory
Cipher 1
Cipher 2
Cipher 4
Register Space
Plain
Plain
Plain + Mask A
Plain
Plain + Mask B
Notes: Leading to a different ciphertext, although the payload stayed the same.
AMD also provided a report this AMD
Transitions: However when implementing these strategies, we cannot look at our program in isolation but must consider the whole software stack

## Slide 54: Software Level Mitigations: Secure Registers
Memory
Ciphertext
HV
VM User
VM OS
Plain + Mask A
Plain
Plain + Mask B
Notes: This is because there are two sources of context switches, which could leak our unmasked secret value into a fixed memory location,
where our countermeasures do not apply

## Slide 55: Software Level Mitigations: Secure Registers
Memory
VMSA
Ciphertext
HV
VM User
VM OS
HV VM Context Switch
Plain + Mask A
Plain
Plain + Mask B
Notes: The first one is the HV VM context switch, where the VMs register values get written into a memory structure called VMSA that is at a fixed loation.
Thus the attacker can leak the secret from the VMSA

## Slide 56: Software Level Mitigations: Secure Registers
Memory
VMSA
Ciphertext
HV
VM User
VM OS
HV VM Context Switch
AMD patch adds
Freshness
Plain + Mask A
Plain
Plain + Mask B
Notes: This was exploited in an earlier paper and AMD provided a firmware patch, which adds freshness to this page.
However note, that the VMSA is just a single fixed page, so the cost is relatively low

## Slide 57: Software Level Mitigations: Secure Registers
Memory
VMSA
pt_regs
Ciphertext
HV
VM User
VM OS
OS Context Switch
HV VM Context Switch
AMD patch adds
Freshness
Plain + Mask A
Plain
Plain + Mask B
Notes: The second context switch is the OS context switch inside the VM, e.g. to schedule between different processes.
Again the register values are written to a fixed location.

## Slide 58: Software Level Mitigations: Secure Registers
Memory
VMSA
pt_regs
Ciphertext
HV
VM User
VM OS
OS Context Switch
HV VM Context Switch
AMD patch adds
Freshness
Our Kernel patch
Randomizes Position
Plain + Mask A
Plain
Plain + Mask B
Notes: We have provided a POC patch to fix this problem by randomizing the location of pt_regs
Thus we have a now foundation to implement automated tools for securing user space processes in future work

## Slide 59: Software-level mitigation – Securing Register Space
Cannot build dictionary
Process 1
Kernel
Context Switch
Pt_regs
Kernel patch -- Randomize pt_regs during context switch
Foundation for securing user space applications
gPA1
Process 1
Kernel
Pt_regs
gPA2
Notes: Luca: “How about PCB” what is this refering to? Our discussion of entry stack vs thread stack on webex? Mengyuan: Yes.

## Slide 60: Ciphertext Side Channels
SEV
VMM
VM
AMD CPU
VM
VMSA
The whole memory
We
Show that the ciphertext side channel affects the whole VM memory
Show end-to-end attacks that can steal crypto keys in most state-of-the-art crypto libraries
Discuss the ciphertext side channel’s potential threat to other memory-encryption based TEEs (SEV, TDX, CCA)
Notes: We show that the ciphertext side channel affects the whole VM memory
And underlined this by several end to end attacks against state of the art constant ime crypto libraries
Furthermore we discussed the potential applicability to other TEE designs

## Slide 61: Summary
Most TEEs adopt deterministic encryption
Ciphertext-plaintext 1-to-1 mapping
Enable inferring plaintext via ciphertext
Leak secret from the ciphertext of kernel structure, heap, and stack
Software or Hardware countermeasures are needed
CVE-2021-46744
UzL-ITS/sev-ciphertext-side-channels
Notes: Thanks you
We are happy to answer questions now